## Slide 1
RoboNav: Robot Navigation in Dynamic Environment using Deep Reinforcement Learning
Group 7: Abhishek Jain, Kavit Nilesh Shah, Kenechukwu C. Mbanisi, Sanjeev Kannan
Guided By: Prof. Yanhua Li
<number>

## Slide 2
Where we’re headed!
<number>
Notes: What we wanted our project to do :
Want to do.

## Slide 3
Introduction
Mobile Robot Navigation
Decide between several factors :
  Shortest Distance Path
  Obstacle avoidance
  Least Time
  Partially observable states
<number>

## Slide 4
Classical Mobile Robot Navigation Methods
  Pipeline : Perception -> Planning -> Control [1]
  Latest Methods include : SLAM [2], D*
Drawbacks with Classical Methods:
  Perception, Making sense of data - high processing GPU required
  Require Re-planning when obstacle is encountered
Reinforcement Learning - addresses most shortcomings
  Only Laser Data - no “perception” or “prediction” required
<number>
Related Work
[1] http://wiki.ros.org/move_base
[2] Durrant-Whyte, Hugh, and Tim Bailey. ”Simultaneous localization and mapping: part I.” IEEE robotics & automation magazine 13.2 (2006): 99-110
[3] https://www.researchgate.net/figure/From-a-modular-pipeline-to-a-perception-planning-deep-neural-network-approach-for_fig1_334049155
Software Pipeline for Mobile Robot Navigation[3]
Notes: No prediction, perception - less compute

## Slide 5
Problem Formulation : Navigating an RL agent to a goal destination in a closed environment with static and moving obstacles
<number>
Methodology
Observation Space :
Laser Scan Data
Current position
Orientation
Action Space :
Discrete
Linear Velocity Vx = {0.15}
Angular Velocity wz = {-1.5, -0.75, 0.0, .075, 1.5} rad/s
Continuous
Linear Velocity Vx = {0.15} m/s
Angular Velocity wz = [-2,2] rad/s
Rewards :
+ve :
Getting close to Goal,
heading towards goal
-ve :
Increasing Distance from Goal
heading away from goal

## Slide 6
Deep Q Network
1 x Input Layer
2 x Fully Connected Layers
1 x Output Layer
<number>
Neural Net Architecture
DDPG
1 x Input Layer (26 units)
1 x Batch Normalization Layer
3 x Fully Connected Layers
1 x output Layer
Notes: Action Space : move to

## Slide 7
Stage 1
Stage 2
Stage 3
Stage 4
<number>
Experiments: Simulation Environments

## Slide 8
Traditional ROS Navigation Stack Library
Employs a hierarchical motion planner with following submodules:
  Global Planner : Computes a higher level path
  Local Planner : Computer more fine-tuned local path
  Controller
Works with both static and dynamic environment
Tries to find the “best” possible path from start to goal
<number>
Experiments: Baseline (Move-Base)

## Slide 9
Number of trials : 10
Number of goal per trial: 5
Data used to compute the metrics: x,y coordinates, distance to obstacles and velocities
Metrics:
Success Rate
Path Length
Clearance
<number>
Experiments: Evaluation Metrics

## Slide 10
STAGE 1
<number>
Simulation Results
Untrained Agent
Trained Agent

## Slide 11
STAGE 1
No major obstacles
Static Environment
All the 3 agents perform good
<number>
Simulation Results

## Slide 12
<number>
Simulation Results
STAGE 2
Untrained Agent
Trained Agent

## Slide 13
<number>
Simulation Results
STAGE 2
Some obstacles in form of cylindrical poles
Static Environment
DDPG and Move-Base agents give good performance while the DQN agent falters in some trials

## Slide 14
<number>
Simulation Results
STAGE 3
Untrained Agent
Trained Agent

## Slide 15
<number>
Simulation Results
STAGE 3
Fixed moving obstacles in form of cylindrical poles
Dynamic Environment
DDPG agent gives good performance while the DQN and Move-Base agents perform poorly.

## Slide 16
<number>
Simulation Results
STAGE 4
Untrained Agent
Trained Agent

## Slide 17
<number>
Simulation Results
STAGE 4
Random moving obstacles in form of cylindrical poles coupled with fixed obstacles in form of rectangular walls
Dynamic Environment
DDPG and Move-Base agents gives good performance while the DQN agent performs poorly.

## Slide 18
<number>
Simulation Results
STAGE 5
Novel dynamic environment
None of the agents were trained in this environment
All 3 agents perform good

## Slide 19
2 different types of DRL agents were used: DQN and DDPG
DQN learns faster as compared to DDPG while DDPG gives better control and smoother trajectories than DQN.
DDPG gives better accuracy than DQN owing to its continuous action-space.
Move-Base tends to fail in dynamic environment while DRL agents give appreciable performance.
Number of Episodes
Average Reward ( 30 ep.)
DQN
DDPG
<number>
Discussion

## Slide 20
Dense laser scans
Map-based approach
Including observation history
Normalizing laser scan information
Expanding action space (linear vel)
Sensor fusion (LiDAR + camera) for better scene/environment understanding
360 Samples
24 Samples
Map-based Approach
<number>
Future Work